## Slide 1
Assembling & Disassembling the System Hardware Components of the Personal Computer
Objective

## Slide 2
1. Setting the Cabinet ready:-
• Check how to open the cabinet and determine where to fix the components.
• Determine if the case has the appropriate risers installed.
Setting the Cabinet ready

## Slide 3
2. Fitting the Mother board.
• Line up the patch on the motherboard (ps/l, USB, etc ) with the appropriate holes in the block panel I/O shield of the case.
• Check the points where you and to install
• Install them and make the mother board sit on them and fix screws if required.
Fitting the Mother board.

## Slide 4
3. Installing the CPU
• Raise the small lever at the side of the socket.
• Notice that there is a pin missing at one corner, determine the direction to fit in the processor.
• You should not force the CPU. When inserting it. All pins should slide smoothly into the socket.
• Lock the lever back down.
Installing the CPU

## Slide 5
4. Installing CPU fan
• Install the heat sink over it (Different type for each processor). Heat sink
/CPU fan.
Installing CPU fan

## Slide 6
5. Fitting the RAM:
• The RAM must be suitable for motherboard.
• There are currently 3 types of RAM available.
a) SD RAM.
b) DDR SD RAM.
c) RD RAM.
• The mother board‘s chipset determines which type of RAM may be used.
Fitting the RAM

## Slide 7
6. Installing SMPS
Switch mode power supply, SMPS: The term switch mode power supply is generally used to indicate an item that can be connected to the mains, or other external supply and used to generate the source power. In other words it is a complete power supply.
Switch mode regulator: This typically refers just to the electronic circuit that provides the regulation. A switch mode regulator will be part of the overall switch mode power supply.
Switch mode regulator controller: Many switch mode regulator integrated circuits do not contain he series switching element. This will be true if the current or voltage levels are high, because an external series switching element would be able to better handle the higher current and voltage levels, as well as the resultant power dissipation.
Installing SMPS

## Slide 8
7. Installing the ATX Power Connector ATX Connectors:
• PS, Mouse.
• Key board.
• USB.
• Parallel ( Prints )
• Serial COM1.
• Serial COM 2.
• Joystick.
• Sound.
Installing the ATX Power Connector ATX Connectors

## Slide 9
8. Installing the HDD and Floppy disk:
Place the floppy and hard disks in their slots.
Leave some space above HDD to prevent heat building.
Check the jumper configuration.
Fix the screws.
Installing the HDD and Floppy disk

## Slide 10
9. CD ROM Drive :
• CD-ROM drive is similar to installing a hard disk.
• 1st check that the jumper configuration is correct.
• Fix the screw.
CD ROM Drive

## Slide 11
LAN Card
1. Assemble your materials.
Gather up the network card and the driver disks. While you’re at it, get your Windows installation CD just in case.
2. Shut down Windows, turn off the computer and unplug it.
3. Remove the cover from your computer.
4. Find an unused expansion slot inside the computer.
5. Remove the metal slot protector from the back of the computer’s chassis
6. Insert the network interface card into the slot.
7. Secure the network interface card.
8. Put the computer’s case back together.
9. Plug in the computer and turn it back on.
LAN Card

## Slide 12
11. Connecting the ribbon Cables and Front panel connections
• Attach the long end of the cable to the IDEU connector on the motherboard first. The red stripe on the IDE cable should be facing the CD Power.
Connecting the ribbon Cables and Front panel connections

## Slide 13
12. Final Check:
• Mother board jumper configurations are the settings for the processor operator.
• Drive jumper settings, master/ slave correct?
• Is the processor, RAM modules and plug in cards finally seated in their sockets?
• Did you plug all the cables in? Do they all fit really?
• Have you frightened all the screws in plug- in cards or fitted the clips?
• Are the drive secure?
• Have u connected the power cables to all driver?
Final Check

## Slide 14
Powering up for the first time:
1. Ensure that no wires are touching the CPU heat sink fan.
2. Plug your monitor, mouse and keyboard.
3. Plug in power card and switch the power supply.
4. If everything is connected as it should be
• All systems, fans should start spinning
• U should hear a single beep and after about 5-10 sec
• Amber light on monitor should go green
• You will see computer start to boot with a memory check
• Now check front LED‘S to see if u plugged them in correctly
• Check all other buttons
• Power afford change any wrong settings

## Slide 15
Why should one learn about hardware?
Troubleshoot you and save time.
Knowing about system internals and components.
Very easy installation for modern hardware.
Install extra memory.
Removing components.
Why should one learn about hardware?

## Slide 16
Viva Q & A :
Define hardware?
Define software?
What are the functional units of a computer?
IDE Stands for
What are the other names for LAN card
What is the use of LAN card?
Viva Questions

## Slide 17
Reference
1. Hardware Bible by Winn L. Rosch
2. Hardware and Software of Personal Computers by Sanjay K. Bose
3. Fundamentals of Computers by V. Rajaraman
4. Computer Studies - A first course by John Shelley and Roger Hunt
5. Computer Fundamentals, MS Office and Internet & WebTechnology by Dinesh Maidasani
6. Modern Computer Hardware Course by M Lotia, P Nair, P Lotia
Reference